## Slide 1: Design Review 2
Team 3: Chandler Kuhn, Jack Sann, Bryan Hasselman, William Ho, Sam Coyle, Chris Sheehan
December 6, 2023
Notes: Good afternoon everyone
Names

## Slide 2: Outline
Project Objectives & Schedule
Mission Design
Sizing Inputs
Sizing Results
Aircraft Configuration
Anticipated Risks
Future Milestones
Summary
Notes: The purpose of this design review is to document the initial project work, explain the basis for decisions, and elicit feedback and suggestions from the reviewers.

## Slide 3: High-Level Objectives
Design an aircraft that can circumnavigate the world without refueling
Set record for fastest prop-driven airplane to circumnavigate, according to FAI guidelines
Honor the legacy of the Rutan Voyager
Notes: High-level objectives of the project from when we were tasked with the project
Circumnavigate the world
Set FAI record for SPEED
Federation Aeronautique Internationale

## Slide 4: Competing Systems
Rutan Voyager (1986)
Record: Fastest propeller-driven aircraft around the world
Mission Range: 24,986 miles
Engine: Modified Continental O-200/240
Virgin Atlantic GlobalFlyer (2005)
Record: Fastest jet aircraft around the world record
Mission Range: 25,766 miles
Engine: Modified Williams International FJ44 turbofan
Source: National Air and Space

## Slide 5: Mission Design
FAI Sporting Code Section 2, part 4.6.4: Speed Around the World, Nonstop and Non-refueled
Minimum Distance: 36,770km (19850 nm)
Pre-declared closed-circuit course
No landing or refueling
Cross all meridians
Lateral limits: +/- 66°
Considerations
Record (FAI)
Safety
Profitability
Record Speed =
Notes: Develop requirements for our program based off the needs of our stakeholders
Requirements explored in depth later in presentation
Internal:
  Program Schedule
  Logistics
External
  Mission Profile
  Support
End-User
  Safety

## Slide 6: Program Schedule
Current Status: Initial Design
Complete: Mission Design, Sizing, Configuration
Upcoming: Subsystem Design
Notes: Timeline of the overall program
  From company management
Time: Ready to test by Jan. 2027
  3 and a half year program
Design Complete: Jan. 2025
Manufacturing Complete: June 2026
  18 months to manufacture

## Slide 7: Flightpath Design
Atmosphere
Wind
Weather
Altitude
Terrain
Supplemental Oxygen
Safety
Available Diversion Runways
No-Fly Zones
Mission Parameters
Range: 20,650 nm
Cruise TAS: 110 knots
Considerations
Time: 170 hours
Dual Crew Weight: 300 lbs
Payload Weight: 300 lbs
Notes: Mission Range: 38,250 km
  Length of flightpath
Capable Range: 43,570 km​
  Account for margin of safety
Mission Time: 180 hours​
  Nominal mission time
Capable Flight Time: 205 hours
  Maximum flight time of aircraft
Takeoff Distance: 12,000 feet
  Runway distance is 14,000
Ground Speed: 115 knots​
  Ground speed needed throughout flight
  110 TAS, 10% faster than Voyager
Altitude: 8,000 feet​
(Assumption: average tail wind speed of 12 knots)

## Slide 8: Mission Design
Takeoff & Landing Location: Edwards AFB, CA
Takeoff Distance: 14,000 ft
Average Cruise Altitude: 9,000 ft
  Starting: 6,000 ft
  End: 12,000 ft
Average Wind Speed: 17 knots
Cruise Ground Speed: 127 knots
1. Warm-up and Takeoff
2. Climb
3. Cruise
-Increase altitude over time
4. Descent
5. Landing
Direction: East
Terrain avoidance
Notes: Mission Range: 20,560 nm
  Length of flightpath
Capable Range: 23,500 nm​
  Account for margin of safety
Mission Time: 180 hours​
  Nominal mission time
Capable Flight Time: 205 hours
  Maximum flight time of aircraft
Takeoff Distance: 12,000 feet
  Runway distance is 14,000
Ground Speed: 115 knots​
  Ground speed needed throughout flight
  110 TAS, 10% faster than Voyager
Altitude: 6,000 – 12,000 ft
(Assumption: average tail wind speed of 17 knots)

## Slide 9
Mission Flightpath
⟷ Mission flightpath
⟷ Voyager flightpath
● Edwards AFB
❖ No-fly zones
⟷ FAI Flight Limits
●
0°
30°
60°
90°
120°
150°
180°
- 30°
- 90°
- 120°
- 150°
- 180°
0°
- 30°
- 45°
- 66°
- 60°
- 15°
15°
30°
45°
66°
● Edwards AFB
⟷ FAI Flight Limits
⟷ Subtropic Belts
❖ No-fly zone
Notes: Mission Profile: 5 phases of flight with mission parameters
  Conservative estimate of time, speed, altitude, distance for each phase
  Takeoff and climb:
    <12,000 feet of runway: runway is 14,000 feet, voyager took 14,000 feet
    climb at relatively slower rate to conserve fuel
    During daylight
    Climb 2300 feet mountain in front of takeoff, 47 nautical miles 87 km away, With safety factor of 1000 feet
  Cruise:
    Slightly faster than the Rutan Voyager (100 knots)
    Time: around 182 hours, roughly less than 8 days

## Slide 10
Average Wind Patterns
⟷ Mission flightpath
40
35
30
25
20
15
10
5
0
Wind Speed (knots)
0°
30°
60°
90°
120°
150°
180°
- 30°
- 90°
- 120°
- 150°
- 180°
0°
- 30°
- 45°
- 66°
- 60°
- 15°
15°
45°
66°
30°
● Edwards AFB
⟷ FAI Flight Limits
⟷ Subtropic Belts
12000’
6000’
7000’
8000’
9000’
10000’
11000’
Altitude
55
50
45
●
Notes: 8000 feet​
Would NOT require pressurization or oxygen​
Do not factor in specific monthly (February) winds​
​
Convective Atmospheric Potential Energy​
Stronger north and south of the high pressure belts​
Source: MATLAB
They used U.S. Naval Research Laboratory Horizontal Wind Model (HWM™) to calculate the meridional and zonal components of the wind

## Slide 11
20,000
15,000
10,000
5,000
Altitude (ft)
True Air Speed (kts)
100
140
180
60
CAS = 45
CAS = 65
Absolute Ceiling: 18,000 ft
CAS = 85
CAS = 105
CAS = 125
CAS = 145
CAS = 165
Notes: So this is the flight env that we will be designing to. You can see here our initial cruise condition at 6000 ft 110kts, and our final at 12000ft 100kts. In case we need to climb over any rough weather our abs celling is set at 18000ft as that is the standard limit or most internal combustion engines. Now if we are at that limit we most likely wont be able to reach our maximum speed of 170 kts, that’s ok, this limit was set based on a dive speed and will be updated as we select an engine.

## Slide 12
Chart: Empty Weight Fraction
| 0.23210233133897257 | 0.16259090909090909 | #N/A | #N/A | #N/A | #N/A | 0.37086973034561338 | #N/A | #N/A | #N/A | #N/A | 0.34283862605314325 | 0.3287764866712235 | 1 | #N/A | #N/A | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Performance | 26366 | 26389.3 | 1300 | 8300 | 18500 | 2500 | 14200 | 4368 | 4488 | 7150 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
UAV | 26366 | 26389.3 | 1300 | 8300 | 18500 | 2500 | 14200 | 4368 | 4488 | 7150 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Airliner | 26366 | 26389.3 | 1300 | 8300 | 18500 | 2500 | 14200 | 4368 | 4488 | 7150 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
L/D ≈ 5 | 16626.0978 | 13680.2223 | 11956.9955 | 10734.3467 | 9785.9866 | 9011.12 | 8355.9796 | 7788.4712 | 7287.8933 | 6840.1111 | 6435.0429 | 6065.2445 | 5725.063 | 5410.1041 | 5116.8844 | 4842.5957 | 4584.9411 | 4342.0178 | 4112.2321 | 3894.2356 | 3686.8774 | 3489.1673 | 3300.2474 | 3119.369 | 2945.8755 | 2779.1875 | 2618.7911 | 2464.2286 | 2315.0905 | 2171.0089 | 2031.6522 | 1896.7202 | 1765.9406 | 1639.0655 | 1515.8685 | 1396.1423 | 1279.6966 | 1166.3566 | 1055.9608 | 948.3601 | 843.4165 | 741.0019 | 640.9973 | 543.2918 | 447.7822
L/D ≈ 15 | 49878.2933 | 41040.6668 | 35870.9866 | 32203.0402 | 29357.9599 | 27033.3601 | 25067.9389 | 23365.4137 | 21863.68 | 20520.3334 | 19305.1286 | 18195.7335 | 17175.189 | 16230.3124 | 15350.6533 | 14527.7871 | 13754.8232 | 13026.0534 | 12336.6963 | 11682.7068 | 11060.6322 | 10467.502 | 9900.7421 | 9358.107 | 8837.6266 | 8337.5625 | 7856.3733 | 7392.6858 | 6945.2715 | 6513.0267 | 6094.9565 | 5690.1606 | 5297.8219 | 4917.1966 | 4547.6055 | 4188.4269 | 3839.0899 | 3499.0698 | 3167.8823 | 2845.0803 | 2530.2495 | 2223.0057 | 1922.9918 | 1629.8755 | 1343.3466
L/D ≈ 25 | 83130.4889 | 68401.1113 | 59784.9777 | 53671.7337 | 48929.9332 | 45055.6001 | 41779.8982 | 38942.3561 | 36439.4666 | 34200.5556 | 32175.2143 | 30326.2226 | 28625.315 | 27050.5206 | 25584.4221 | 24212.9785 | 22924.7053 | 21710.089 | 20561.1606 | 19471.1781 | 18434.3871 | 17445.8367 | 16501.2368 | 15596.845 | 14729.3776 | 13895.9374 | 13093.9555 | 12321.143 | 11575.4525 | 10855.0445 | 10158.2608 | 9483.6009 | 8829.7032 | 8195.3277 | 7579.3426 | 6980.7114 | 6398.4832 | 5831.783 | 5279.8039 | 4741.8005 | 4217.0824 | 3705.0095 | 3204.9864 | 2716.4591 | 2238.911
L/D ≈ 35 | 116382.6844 | 95761.5558 | 83698.9688 | 75140.4272 | 68501.9065 | 63077.8402 | 58491.8575 | 54519.2985 | 51015.2532 | 47880.7779 | 45045.3 | 42456.7116 | 40075.441 | 37870.7289 | 35818.1909 | 33898.1699 | 32094.5874 | 30394.1246 | 28785.6248 | 27259.6493 | 25808.1419 | 24424.1714 | 23101.7315 | 21835.583 | 20621.1286 | 19454.3124 | 18331.5376 | 17249.6002 | 16205.6335 | 15197.0623 | 14221.5651 | 13277.0413 | 12361.5845 | 11473.4588 | 10611.0796 | 9772.996 | 8957.8765 | 8164.4962 | 7391.7254 | 6638.5207 | 5903.9154 | 5187.0133 | 4486.981 | 3803.0428 | 3134.4753
L/D = 5
L/D = 15
L/D = 25
L/D = 35
Notes: This graph shows the empty weight fraction vs range for various aircraft . The lines of constant L/D show how far an aircraft would go with that L/D at a given empty weight fraction. Immediately we can see that if we want to achieve our range an have an achievable L/D we need to be in this range here. Some things to note is that our design target is on roughly the same L/D curve as the rutan voyager hoever the empty weigh fraction is higher. We are able to set this more conservative empty weight fraction with the same L/D because we are planning on traveling less distance while still breaking the record.

## Slide 13: Initial Sizing Inputs
Competitive Assessment
L/D: 20-28
SFC: 0.30-0.40
We/Wto: 0.20-0.28
CLmax : 1.5
e: 0.80
CD0: 0.017
Mission Design
Range: 20650 nmi
Payload Weight: 600 lbs
Altitude: 9,000 ft
Cruise: 110 KTAS

## Slide 14
Mission Range = 20650 nmi, Payload Weight = 600 lbs, EWF = 0.24
L/D = 22
SFC = .300
16,000
18,000
14,000
12,000
10,000
8,000
6,000
4,000
MTOW (lbs)
L/D = 24
L/D = 26
L/D = 28
L/D = 20
SFC = .325
2,000
20,000
SFC = .375
SFC = .350
SFC = .400

## Slide 15
Mission Range = 20650 nmi, Payload Weight = 600 lbs, SFC = .350
16,000
18,000
14,000
12,000
10,000
8,000
6,000
4,000
MTOW (lbs)
2,000
20,000
L/D = 20
L/D = 22
L/D = 24
L/D = 26
L/D = 28
EWF = .20
EWF = .22
EWF = .24
EWF = .26
EWF = .28

## Slide 16: Lift Analysis
Inputs
Cruise Speed: 110 KTAS
Avg. Weight: 6,200 lbs
L/D: 23
CD0
Outputs
CL
W/S
AR
Competitive Assessment
Mission Design
Configuration
Notes: Estimates of Empty Weight Ratio
  Main part of briefing
Group Weight Calculations
  Started, covered at end of briefing
  started calcs on empty weight
Build-Up Weight Calculation
  Input when plane subsystems are designed, input individual parts
Weighing of Actual Parts
  Weight actual parts during detail design, manufacturing
  Compare to estimates and calculations

## Slide 17
Wing Loading (lbs/ft^2)
22
24
26
28
30
32
34
36
38
40
AR = 24
AR = 28
AR = 32
AR = 36
AR = 40
CD0 = 0.017
CD0 = 0.019
CD0 = 0.021
CD0 = 0.023
CD0 = 0.025
e = 0.8, VTAS = 110 knots, Average Mission Weight = 6,200 lbs

## Slide 18
Wing Loading (lbs/ft^2)
22
24
26
28
30
32
34
36
38
40
AR = 24
AR = 28
AR = 32
AR = 36
AR = 40
CD0 = 0.017
CD0 = 0.019
CD0 = 0.021
CD0 = 0.023
CD0 = 0.025
e = 0.8, VTAS = 110 knots, Average Mission Weight = 6,200 lbs
CD0 = 0.019
CD0 = 0.021

## Slide 19
Lift Coefficient
Wing Loading (lb/ft2)
Max-Weight Cruise
Min-Weight Cruise
Average Cruise

## Slide 20
W/S ()
20
Sam Coyle
L/D = 23, CLmax = 1.5, e = 0.8, CD0 = .017
P/W ()
.07
.06
.05
.04
.03
20
30
40
50
Cruise
@6,000 feet, 110 knots
Takeoff = 14,000 ft
Wto @Edwards AFB
Climb
@4% gradient
Landing = 14,000 ft
Wto @Edwards AFB
10
.02
.01
Notes: Using assumed aerodynamic coefficients, variables for relations based on requirements
Takeoff: < 14,000 feet
  Takeoff from runway at EFB
  Using takeoff parameter which is based on takeoff requirement from FAR 23
Cruise: at 8000 feet, 110 knots
  Using power index, based on cruise speed
  From mission design
Climb: > 4% climb gradient
  According to CFR (code of federal regulations)
  Requirement will be investigated further if necessary
Landing: < 14,000 feet
  Worst Case Scenario: need to return to Edwards after failure upon takeoff
    Other scenarios better since weight will be less

## Slide 21: Sizing Results
Weight Calculation
Wf: 2400 lbs
Wfuel: 7000 lbs
Wto: 10000 lbs
EWF: .24
Power Calculation
P/Wto : .04
Takeoff Power: 350 hp
Cruise Power: 100 hp
SFC: .35
Wing Design
Wto/S: 35.5
AR: 37.5
Wing Area: 280 ft2
L/D: 23
Assumptions: e = 0.8, CD0 = .017, CLmax= 1.5

## Slide 23
WING
Aspect Ratio: 37.5 | Wto/S: 35.5 lbs/ft2
Root Chord: 36 in | Tip Chord: 24 in
Wingspan: 94 ft | Wing Area: 120 ft2
FUEL
Total Fuel Volume | 7000 lbs, 1044 gal, 140 ft3
Wing Fuel Volume | 2200 lbs, 328 gal, 44 ft3
Fuselage Volume | 4800 lbs, 716 gal, 96 ft3

## Slide 24
POWER
Total Horsepower (Cruise/Takeoff) | 100/350 hp
Engine #1 | 130 hp
Engine #2 | 220 hp
CABIN
Length | 7.5 feet
Width | 4.0 feet
Height | 3.8 feet

## Slide 25: Preliminary Weight Statement
Item​ | Mass (lbs)​ | FS (in)​ | BL (in)​ | WL (in)​
Structure​ | ​-- | ​0.6 | ​0 | -0.25
Subsystems​ | ​-- | ​0.5 | ​0 | ​-0.4
Empty Weight​ | 2400.0​ | ​0.55 | ​0 | ​-0.325
Crew​ | 300.0​ | ​0.5 | ​0 | ​-0.65
Payload​ | 300.0​ | 0.4 | 0 | ​-0.75
Fuel​ | 7000.0​ | ​0.6 | ​0 | ​-0.25
Takeoff Weight​ | 10000.0​ | ​0.52 | 0 | ​-0.46
Future Steps:
Wing Design
Tail Design
Fuselage Design
Landing Gear Design
Subsystems Concept Design

## Slide 26
Notes: Complete: Competitive Assessment, Mission Design, Requirements
  Used to create sizing inputs
Upcoming: Sizing, Quad Chart, Three-View Drawing, Design Review #2
  Use sizing inputs to work on final sizing results in two weeks

## Slide 27: Program Schedule
Timeline: Record Flight February 2027
Design Complete: March 2025
Manufacturing Complete: June 2026
Notes: Timeline of the overall program
  From company management
Time: Ready to test by Jan. 2027
  3 and a half year program
Design Complete: Jan. 2025
Manufacturing Complete: June 2026
  18 months to manufacture

## Slide 28: Program Risks
Technical
Engine: Ability to function for entirety of mission
Parasitic Drag Coefficient (CD0): Accuracy of variable
Operational
Schedule: Ability to stay on track in the future
Weather: Unforeseen conditions
Notes: Specific Implications, assumptions
Engine
Be specific about variables that are uncertain
More about assumptions that are difficult to justify as rational thus far as oppose to things that we need to study
Questions:
Be honest, upfront- don’t make up somthing
Idk, Say when we will know

## Slide 29: Upcoming Milestones
Trade Studies
Objective: Compare design types and configurations for profiles
Approach:
  Performance
  Aerodynamics
  Structure
  Feasibility
Subsystem Design
Objective: Design profiles and determine impact on configuration
Profiles:
  Wing
  Tail
  Fuselage
  Landing Gear

## Slide 30: Summary
Project and Mission Scope Overview
Sizing Approach & Inputs
Sizing Results & Design Sensitivities
Aircraft Configuration & Characteristics

## Slide 31: Mission Design
Takeoff & Landing Location: Edwards AFB, CA
Takeoff Distance: 14,000 ft
Average Cruise Altitude: 9,000 ft
  Starting: 6,000 ft
  End: 12,000 ft
Average Wind Speed: 17 knots
Cruise Ground Speed: 127 knots
1. Warm-up and Takeoff
2. Climb
3. Cruise
-Climb
4. Descent
5. Landing
Direction: East
-Terrain avoidance
Notes: Mission Range: 38,250 km
  Length of flightpath
Capable Range: 43,570 km​
  Account for margin of safety
Mission Time: 180 hours​
  Nominal mission time
Capable Flight Time: 205 hours
  Maximum flight time of aircraft
Takeoff Distance: 12,000 feet
  Runway distance is 14,000
Ground Speed: 115 knots​
  Ground speed needed throughout flight
  110 TAS, 10% faster than Voyager
Altitude: 8,000 feet​
(Assumption: average tail wind speed of 12 knots)

## Slide 32: Flightpath Design
Weather
Wind
Inclement Weather
Altitude
Terrain
Oxygen Levels
Safety
Available Runways
No-Fly Zones
Notes: Mission Range: 38,250 km
  Length of flightpath
Capable Range: 43,570 km​
  Account for margin of safety
Mission Time: 180 hours​
  Nominal mission time
Capable Flight Time: 205 hours
  Maximum flight time of aircraft
Takeoff Distance: 12,000 feet
  Runway distance is 14,000
Ground Speed: 115 knots​
  Ground speed needed throughout flight
  110 TAS, 10% faster than Voyager
Altitude: 8,000 feet​
(Assumption: average tail wind speed of 12 knots)

## Slide 33: Mission Design
Requirements
Mission Range: 20,650 nm
Cruise TAS: 110 knots
Considerations
Mission Time: 170 hours
Dual Crew Weight: 300 lbs
Payload Weight: 300 lbs
Item | Rationale | Weight (lbs)
Pilots & Parachutes |  | 300
Water |  | 112
Food |  | 48
Life Vest |  | 5
Emergency Raft |  | 15
Clothing |  | 30
Miscellaneous Items |  | 40
Oxygen |  | 50
Total Payload Weight | -- | 600
Notes: Mission Range: 38,250 km
  Length of flightpath
Capable Range: 43,570 km​
  Account for margin of safety
Mission Time: 180 hours​
  Nominal mission time
Capable Flight Time: 205 hours
  Maximum flight time of aircraft
Takeoff Distance: 12,000 feet
  Runway distance is 14,000
Ground Speed: 115 knots​
  Ground speed needed throughout flight
  110 TAS, 10% faster than Voyager
Altitude: 8,000 feet​
(Assumption: average tail wind speed of 12 knots)

## Slide 34
Average Wind Patterns
⟷ Mission flightpath
● Edwards AFB
⟷ FAI Flight Limits
⟷ Subtropic Belts
40
35
30
25
20
15
10
5
0
Wind Speed (knots)
●
0°
30°
60°
90°
120°
150°
180°
- 30°
- 90°
- 120°
- 150°
- 180°
0°
- 30°
- 45°
- 66°
- 60°
- 15°
15°
45°
66°
30°
Notes: 8000 feet​
Would NOT require pressurization or oxygen​
Do not factor in specific monthly (February) winds​
​
Convective Atmospheric Potential Energy​
Stronger north and south of the high pressure belts​
Source: MATLAB
They used U.S. Naval Research Laboratory Horizontal Wind Model (HWM™) to calculate the meridional and zonal components of the wind

## Slide 35
Average Wind Patterns
⟷ Mission flightpath
● Edwards AFB
⟷ FAI Flight Limits
⟷ Subtropic Belts
40
35
30
25
20
15
10
5
0
Wind Speed (knots)
●
0°
30°
60°
90°
120°
150°
180°
- 30°
- 90°
- 120°
- 150°
- 180°
0°
- 30°
- 45°
- 66°
- 60°
- 15°
15°
45°
66°
30°
⟷ Mission flightpath
Notes: 8000 feet​
Would NOT require pressurization or oxygen​
Do not factor in specific monthly (February) winds​
​
Convective Atmospheric Potential Energy​
Stronger north and south of the high pressure belts​
Source: MATLAB
They used U.S. Naval Research Laboratory Horizontal Wind Model (HWM™) to calculate the meridional and zonal components of the wind

## Slide 37
Wind Patterns
40
35
30
25
20
15
10
5
0
Wind Speed (knots)
●
0°
30°
60°
90°
120°
150°
180°
- 30°
- 90°
- 120°
- 150°
- 180°
0°
- 30°
- 45°
- 66°
- 60°
- 15°
15°
45°
66°
30°
Altitude: 9,000 feet
Month: February
Notes: 8000 feet​
Would NOT require pressurization or oxygen​
Do not factor in specific monthly (February) winds​
​
Convective Atmospheric Potential Energy​
Stronger north and south of the high pressure belts​
Source: MATLAB
They used U.S. Naval Research Laboratory Horizontal Wind Model (HWM™) to calculate the meridional and zonal components of the wind

## Slide 38: Program Risks
Technical
Record & Mission Viability:
Accuracy of Assumed Variables
Subsystem Design
Performance & Aerodynamic Calcs
Operational
Pilot Safety:
Hazardous Conditions
Weather Modeling
Emergency Procedures
Business
Profitability:
Cost, Marketing
Schedule
Plan of Execution
Specific Implications, assumptions
Engine
Be specific about variables that are uncertain
More about assumptions that are difficult to justify as rational thus far as oppose to things that we need to study
Questions:
Be honest, upfront- don’t make up somthing
Idk, Say when we will know

## Slide 39
WING
Aspect Ratio: 37.5 | Wto/S: 35.5 lbs/ft2
Root Chord: 36 in | Tip Chord: 24 in
Wingspan: 94 ft | Wing Area: 120 ft2
FUEL
Total Fuel Volume | 8000 lbs, _ gal, _ ft3
Wing Fuel Volume | 8000 lbs, _ gal, _ ft3
Fuselage Volume | 8000 lbs, _ gal, _ ft3

## Slide 40
Cruise: 110 kts @ 8,000 feet, e = 0.8, CD0 = .017
Aspect Ratio
Wing Loading ()
30
35
40
45
50
55
50
45
40
35
21
22
23
24
25
26
27
L/D

## Slide 41
Cruise Lift Coefficient = 0.78
Cruise Wing Loading = 35.58
Assumptions: L/Dmax = 23, e = 0.8, Cd0 = 0.017

## Slide 42: Powerplant Considerations
DEL-120
Dry Weight: 360 lbs
Rated Horsepower: 205 Hp
Cruise Horsepower (75% power): 180 Hp
PSFC: 0.345
CD-155
Dry Weight: 295.4 lbs
Rated Horsepower: 155 Hp
Performance Cruise (75% rated): 132 Hp
PSFC: 0.35
Source: Continental, Lycoming

## Slide 43
Business
Proposed Financers
Corporate and Industry Sponsors
Government and Research Sponsors
Philanthropic and Sustainability Organizations
Venture Capital & Private Equity
Major Expenses
Materials
Labor
Manufacturing
Test
Execution
Notes: Develop requirements for our program based off the needs of our stakeholders
Requirements explored in depth later in presentation
Internal:
  Program Schedule
  Logistics
External
  Mission Profile
  Support
End-User
  Safety

## Slide 44
Proposed Financers
Corporate and Industry Sponsors
Government and Research Sponsors
Philanthropic and Sustainability Organizations
Venture Capital & Private Equity
Major Expenses
Materials
Labor
Manufacturing
Test
Execution
Mission
Cross all nav-points
Communicate Telemetry
Verify Flight Performance
Emergency Outcomes
Mid-Flight Emergency Landing
Return to Field
Water Ditching
Business
Operations

## Slide 45: Trade Studies

## Slide 46
e = 0.8, CD0 = .017, L/Dmax = 23, AR = 37.5, W/S = 35.5 lbs/ft2
CL
CD
.2
.6
1.0
1.4
1.8
.01
.02
.03
.04
.05
Max L/D
Takeoff Weight
Empty Weight

## Slide 47: Program Approach
Business
Regulations
Operations
Program Needs
World Record
Safety
Profitability
Notes: Develop requirements for our program based off the needs of our stakeholders
Requirements explored in depth later in presentation
Internal:
  Program Schedule
  Logistics
External
  Mission Profile
  Support
End-User
  Safety

## Slide 48
Mission Range = 20650 nmi, Payload Weight = 600 lbs, L/D = 23
EWF = .20
16,000
18,000
14,000
12,000
10,000
8,000
6,000
4,000
MTOW (lbs)
EWF = .22
2,000
20,000
EWF = ..24
EWF = .28
SFC = .300
SFC = .325
SFC = .350
SFC = .375
SFC = .400
EWF = ..26

## Slide 49: Program Approach
Internal Needs
Profitability
Logistics
Feasibility
External Needs
Mission Parameters
External Safety
Communication
End-User Needs
Marketing
Mission Success
Safety
Internal Stakeholders
Company Management
Engineering Team
External Stakeholders
FAA & other regulatory agencies
FAI
End-Users
Sponsors & Investors
Pilots
Notes: Develop requirements for our program based off the needs of our stakeholders
Requirements explored in depth later in presentation
Internal:
  Program Schedule
  Logistics
External
  Mission Profile
  Support
End-User
  Safety

## Slide 50: Concept of Operations
(1) Takeoff & (5) Landing
(2) Climb
- Both engines on
(3) Cruise
-front engine on
(4) Descent
Ground Support Station
Airport: Edwards AFB, CA
Notes: Flightpath: Depicts 5 phases of flight
Takeoff and land at same airport
Support and Safety: Ground support communicates around the world via satellite, emergency support on standby

## Slide 51
Mission
Cross all nav-points
Communicate Telemetry
Verify Flight Performance
Emergency Outcomes
Mid-Flight Emergency Landing
Return to Field
Water Ditching
Notes: Develop requirements for our program based off the needs of our stakeholders
Requirements explored in depth later in presentation
Internal:
  Program Schedule
  Logistics
External
  Mission Profile
  Support
End-User
  Safety

## Slide 52: Program Sizing Process
Estimates of Sizing Inputs
Group Sizing Calculations
Build-Up Calculations
Testing of Actual Parts
Initial Design
Detail Design
Manufacturing
Notes: Estimates of Empty Weight Ratio
  Main part of briefing
Group Weight Calculations
  Started, covered at end of briefing
  started calcs on empty weight
Build-Up Weight Calculation
  Input when plane subsystems are designed, input individual parts
Weighing of Actual Parts
  Weight actual parts during detail design, manufacturing
  Compare to estimates and calculations

## Slide 53: CL, max Analysis
 | CL,max | CL,max Take-Off | CL, L
Twin engine propeller | 1.2 – 1.8 | 1.4 – 2.0 | 1.6 – 2.5
Regional turboprop | 1.5 – 1.9 | 1.7 – 2.1 | 1.9 – 3.3
Business jets | 1.4 – 1.8 | 1.6 – 2.2 | 1.6 – 2.6
Transport jets | 1.2 – 1.8 | 1.6 – 2.2 | 1.8 – 3.2
Military trainers | 1.2 – 1.8 | 1.4 – 2.0 | 1.6 – 2.2

## Slide 54: Sizing Input Process (Edit to Reflect Reality)
Stakeholder Needs & Requirements
Configuration
We/Wto
SFC
L/D
Breguet Range Eqn.
Constraint Diagram
T/Wto
Wto
Wto/Sref
Output: Wto, We, Wf, Wpayload, Sref, T
Wpayload
Wf/Wto
Notes: Color coded
  Inputs: in yellow, from mission
  Variables: use competitive assessment for this iteration
  Methods: in green
Start with Stakeholders
Constraint Diagram: Will be conducted in the upcoming weeks presented during sizing results
  Wing reference area, thrust